## Slide 1: Falstad
Circuit Simulator

## Slide 2: Falstad Circuit Simulator
Falstad Circuit Simulator is a
  free
  browser-based
  electronics simulation tool that lets you design and test electrical and electronic circuits interactively.
It’s often called "Falstad" because it was created by Paul Falstad.

## Slide 3: Key Features

## Slide 4: How to Access It?
Web version: https://falstad.com/circuit/
No installation needed

## Slide 12: Falstad Circuit Simulator Algorithm
Initialize: Number nodes, initialize voltages, capacitor voltages, inductor currents, and timestep.
Update dynamic element : Convert capacitors and inductors into equivalent resistances/current sources for this time step.
Linearize nonlinear devices: Apply Newton–Raphson iteration for diodes, transistors, etc.
Assemble Circuit Equation matrix and solve : Include resistors, voltage/current sources, dynamic equivalents, and linearized nonlinear elements and Compute node voltages.
Update time-dependent states: Capacitor voltages and inductor currents for the next timestep.
Render visualization: Node voltages (color), branch currents (animated dots), waveforms.
Advance time: Repeat steps 2–8 until simulation end.

## Slide 13: Exercise
An underground parking lot uses LED floodlights powered by a 24 V DC supply from a battery bank.
Each floodlight module has two identical LEDs in series inside its housing, each with a resistance of 5 Ω
There are four floodlight modules connected in parallel to the supply. The cables from the battery bank to the lights have a total resistance of 0.5 Ω The maintenance engineer needs to determine:
The total current drawn from the battery.

## Slide 14
A sine wave passes through a diode /half-wave rectifier, then through an RC circuit
What happens: The integrator smooths the rectified pulses, producing a DC-like output.
Falstad setup: Add AC sine source → diode → resistor → capacitor