## Slide 1
ISDN
Integrated Services Digital Network
One digital pipe for voice, data and video over the telephone network
Course: Telecommunication Engineering
Department of Information & Communication Engineering
Daffodil International University (DIU)
Notes: Welcome the class. Today's lecture: ISDN — Integrated Services Digital Network. Ask: how many networks did we historically need for voice, data and video? ISDN was the first attempt to merge them into ONE end-to-end digital network. Duration: ~50 minutes.

## Slide 2
Learning Objectives
By the end of this lecture you will be able to…
ISDN in Telecommunication · Dept. of ICE, DIU
Define ISDN
Explain the concept, motivation and design goals of the Integrated Services Digital Network.
Describe the channels
Identify B, D and H channels and compute the capacity of BRI and PRI access.
Draw the architecture
Label functional groups (TE1, TE2, TA, NT1, NT2) and reference points (R, S, T, U).
Explain services & protocols
Classify bearer, tele- and supplementary services; outline the D-channel protocol stack.
Evaluate ISDN today
Discuss B-ISDN, the strengths and limits of ISDN, and why DSL/fibre replaced it.
Notes: Run through the five objectives quickly (1 minute). Emphasise that the exam-relevant items are: channel structures (BRI/PRI numbers), reference model, and service classification.

## Slide 3
Before ISDN: The Analog PSTN Problem
ISDN in Telecommunication · Dept. of ICE, DIU
Suppose your home telephone line can simultaneously:
  Make a voice call
  Send a fax
  Browse the Internet
  Conduct a video conference
Can an ordinary analog telephone line do this?
Answer: No.
Traditional telephone systems were designed mainly for voice communication.
The demand for:
Internet
Fax
Video conferencing
File transfer
created the need for a fully digital communication network.
That network is called ISDN.
Notes: Key teaching point: the core network was ALREADY digital (64 kbps PCM after Nyquist sampling at 8 kHz × 8 bits). The bottleneck was the analog local loop. ISDN = digitising the last mile so one line integrates all services. Ask students to recall PCM from earlier lectures.

## Slide 4
Before ISDN: The Analog PSTN Problem
Why the telephone network needed to go digital end-to-end
ISDN in Telecommunication · Dept. of ICE, DIU
The classic PSTN (1960s–80s)
Local loop (subscriber line) carried analog signals only
Designed for one service: 3.1 kHz voice
Data needed modems — limited to ~9.6–56 kbps
Low data rate
Noise and distortion
Separate network for voice and data
Slow modem speed
The digital idea
By the 1980s, switches and trunks were already digital (PCM, 64 kbps). Only the last mile remained analog.
ISDN extends digital transmission all the way to the subscriber — “end-to-end digital connectivity.”
Notes: Key teaching point: the core network was ALREADY digital (64 kbps PCM after Nyquist sampling at 8 kHz × 8 bits). The bottleneck was the analog local loop. ISDN = digitising the last mile so one line integrates all services. Ask students to recall PCM from earlier lectures.

## Slide 5
What is ISDN?
Definition and design goals (ITU-T, 1984 — I-series recommendations)- ISDN converts the old analog telephone network into a digital network capable of carrying multiple services simultaneously.
ISDN in Telecommunication · Dept. of ICE, DIU
Integrated Services Digital Network (ISDN) is a set of communication standards that allows the digital transmission of voice, video, data, and other services over traditional telephone networks.
Integration
Voice, data, fax and video on one subscriber line and one number.
End-to-end digital
Circuit-switched 64 kbps channels with low noise and fast setup.
Standard interfaces
A small set of ITU-T standard sockets and protocols worldwide.
Out-of-band signalling
A separate D channel for call control (based on SS7 concepts).
Notes: Read the ITU-T style definition, then unpack the four pillars. Stress 'Integrated Services' = many services, one network, one line. Mention the standards: ITU-T (formerly CCITT) I-series and Q-series recommendations, first published 1984, revised 1988 (Blue Book).

## Slide 6
ISDN Channel Types
Logical channels multiplexed on the digital subscriber line
ISDN in Telecommunication · Dept. of ICE, DIU
B channel
64 kbps
Bearer channel —
Purpose: Carries user information.
  Can carry:
  Voice
  Data
  Video
Speed: 64 kbps
D channel
16 / 64 kbps
Delta channel —
Purpose: Carries signaling information.
Examples
Dialing
Call setup
Call termination
Speed
BRI: 16 kbps
PRI: 64 kbps
H channel
384 kbps (H0)
1536 / 1920 kbps (H11/H12)
High-rate channel — an aggregated bundle of B channels for video conferencing, fast fax, high-speed data.
Notes: Mnemonic: B = Bearer (user data), D = Delta/Data-signalling (control). Why 64 kbps? PCM voice: 8000 samples/s × 8 bits = 64 kbps — the fundamental building block of digital telephony. H channels: H0 = 6×B = 384 kbps; H11 = 24×B = 1.536 Mbps (US T1 payload); H12 = 30×B = 1.920 Mbps (Europe E1 payload). Signalling is OUT-OF-BAND: control travels on D, never stealing capacity from B.

## Slide 7
Basic Rate Interface (BRI): 2B + D
The residential / small-office access — ITU-T I.430
ISDN in Telecommunication · Dept. of ICE, DIU
One twisted pair carries three multiplexed channels:
B1 — 64 kbps (voice / data)
B2 — 64 kbps (voice / data)
D — 16 kbps (signalling)
Example: talk on B1 while browsing on B2 — or bond both B channels for a 128 kbps data call.
Bit-rate arithmetic
User rate: 2×64 + 16
= 144 kbps
+ 48 kbps framing, sync & maintenance overhead
Line rate = 192 kbps
Notes: BRI = 2B+D. Work the arithmetic on the board: 2(64)+16 = 144 kbps usable; the I.430 frame adds 48 kbps of framing/synchronisation → 192 kbps gross line rate. Uses the EXISTING copper pair (up to ~5.5 km with 2B1Q line coding on the U interface). Up to 8 devices can share the S/T bus (passive bus). Good exam question: why is D only 16 kbps at BRI? Because signalling traffic is bursty and small.

## Slide 8
Primary Rate Interface (PRI)
The business / PBX access — ITU-T I.431
ISDN in Telecommunication · Dept. of ICE, DIU
 | North America / Japan (T1) | Europe / Bangladesh (E1)
Structure | 23B + D | 30B + D
B channels | 23 × 64 kbps | 30 × 64 kbps
D channel | 64 kbps | 64 kbps
Line rate | 1.544 Mbps | 2.048 Mbps
Typical use | PBX trunks, call centres | PBX trunks, ISPs, video links
PRI rides on the standard digital carrier hierarchy: T1 (24 slots) in North America, E1 (32 slots: 30B + D + framing slot) in Europe and Bangladesh.
Notes: PRI targets organisations, delivered over T1/E1. Bangladesh follows the European E1 standard: 30B+D = 30×64 + 64 = 1.984 Mbps + 64 kbps framing (slot 0) = 2.048 Mbps. US: 23×64+64 = 1.536 Mbps + 8 kbps framing = 1.544 Mbps. Note D is 64 kbps here (not 16) — more calls to manage. One D channel can even control several PRIs (NFAS). Quick quiz: how many simultaneous voice calls on one E1 PRI? Answer: 30.

## Slide 9
ISDN Architecture: Functional Groups
Standardised device roles at the customer premises
ISDN in Telecommunication · Dept. of ICE, DIU
TE1 — Terminal Equipment 1
Native ISDN device (digital phone, ISDN fax, router with ISDN port). Connects directly to the S bus.
TE2 — Terminal Equipment 2
Non-ISDN legacy device (analog phone, PC serial port). Cannot connect directly — needs an adapter.
TA — Terminal Adapter
Converts a TE2's interface (e.g. RS-232, analog) into the ISDN format.
NT2 — Network Termination 2
Intelligent local switching/concentration: a PBX or LAN router distributing channels to many terminals.
NT1 — Network Termination 1
Physical-layer boundary device: converts the 4-wire customer bus (S/T) to the 2-wire local loop (U).
Notes: These are FUNCTIONAL groups — roles, not necessarily separate boxes (one product can combine NT1+NT2). TE1 speaks ISDN natively; TE2 does not and needs a TA. NT1 belongs to layer 1 only (line coding, timing, power feeding); NT2 adds layers 2–3 intelligence (a PBX). In North America the customer owns NT1; in Europe the operator provides it.

## Slide 10
Reference Points: R, S, T, U
The standardised interfaces between functional groups
ISDN in Telecommunication · Dept. of ICE, DIU
TE2
TA
NT2
NT1
ISDN Exchange
R
S
T
U
TE1
(TE1 attaches directly at S)
R — between non-ISDN terminal (TE2) and TA (e.g. RS-232, V.35)
S — between terminal (TE1/TA) and NT2: the 4-wire user bus
T — between NT2 and NT1 (electrically identical to S → “S/T”)
U — the 2-wire local loop between NT1 and the exchange
Notes: Draw this chain on the board and have students memorise it: TE2 –R– TA –S– NT2 –T– NT1 –U– Exchange. Memory aid: the letters run R→S→T→U moving toward the network. S and T are electrically identical (hence 'S/T interface' on equipment). U is where the 2B1Q-coded 2-wire loop begins. Classic exam question: 'Draw the ISDN reference model and explain each reference point.'

## Slide 11
ISDN Services
Three service categories defined in ITU-T I.200 series
ISDN in Telecommunication · Dept. of ICE, DIU
Bearer services
Pure transport of information between users (layers 1–3)
Network does not examine or change content
Examples: 64 kbps circuit-switched voice/data, packet-mode data
Teleservices
Full communication capability including terminal functions (layers 1–7)
Network + standardised application
Examples: telephony, Group-4 fax, teletex, videotex
Supplementary services
Enhance a bearer- or teleservice; never stand alone
Examples: calling line ID (CLIP), call waiting, call forwarding, conference calling, closed user group
Notes: Analogy: a bearer service is the delivery truck (just moves bits, layers 1–3); a teleservice is the whole courier company including packaging (layers 1–7, terminal included); supplementary services are the add-ons like tracking and signature-on-delivery. CLIP/caller-ID — now universal — was popularised by the ISDN D-channel signalling.

## Slide 12
ISDN Protocol Architecture
D-channel signalling stack vs. B-channel transport
ISDN in Telecommunication · Dept. of ICE, DIU
D channel (signalling)
Layer 3 — Q.931
Call control: SETUP, ALERTING, CONNECT, DISCONNECT, RELEASE messages
Layer 2 — Q.921 (LAPD)
Link Access Procedure on the D channel: HDLC-based framing, error control, TEI addressing
Layer 1 — I.430 / I.431
Physical: BRI (192 kbps framed) / PRI (T1/E1); line coding, timing, power
B channel (user data)
Only layer 1 is defined by ISDN. Above that, users run anything: PCM voice, PPP, X.25, frame relay, IP…
Key idea: common-channel signalling
Control and user data travel on separate channels — the same principle as SS7 inside the core network.
Notes: Walk through a call: user lifts handset → TE sends Q.931 SETUP over D channel (inside LAPD frames) → network routes via SS7 → far end ALERTING → CONNECT → then the B channel carries speech. Q.921/LAPD is HDLC-derived (compare with LAPB from X.25). Emphasise: ISDN standardises all 3 layers on D, but only layer 1 on B — that's what makes B channels service-transparent.

## Slide 13
Broadband ISDN (B-ISDN)
The 1990s vision beyond 2 Mbps
ISDN in Telecommunication · Dept. of ICE, DIU
Narrowband ISDN (N-ISDN)
Rates: 144 kbps (BRI) – 2 Mbps (PRI)
Circuit switching, fixed 64 kbps channels
Copper local loop
Fine for voice & modest data — too slow for video & multimedia
Broadband ISDN (B-ISDN)
Target rates: 155 / 622 Mbps and beyond
Transfer mode: ATM — fast packet switching with fixed 53-byte cells
Transmission: SONET/SDH over optical fibre
Legacy: ATM ideas shaped QoS; the market ultimately chose IP + Ethernet
Notes: B-ISDN was the ITU's answer to N-ISDN's speed ceiling: keep the 'one integrated network' vision but move to fibre + ATM cell switching. ATM = Asynchronous Transfer Mode, 53-byte cells (48 payload + 5 header), designed for guaranteed QoS. Historically important: ATM dominated telecom backbones in the 90s (and early DSL DSLAMs), but IP/Ethernet won the converged-network war. One-line takeaway: N-ISDN digitised the loop; B-ISDN previewed today's fibre multimedia networks.

## Slide 14
Advantages and Limitations
A balanced engineering assessment
ISDN in Telecommunication · Dept. of ICE, DIU
Advantages
End-to-end digital: low noise, low BER
Multiple services & devices on one line
Fast call setup (~1–2 s vs ~30 s modem)
Guaranteed, symmetric 64/128 kbps
Rich signalling → caller ID, sub-addressing
Limitations
Capacity ceiling: 128 kbps (BRI) is tiny by broadband standards
Circuit-switched & usage-billed — costly for always-on Internet
Expensive terminals, complex provisioning
Arrived slowly — overtaken by DSL, cable and fibre
Notes: Discussion prompt (2 min, pairs): 'If ISDN was so well engineered, why did it fail commercially?' Guide them to: standards took a decade (joke expansion: 'It Still Does Nothing'); per-minute pricing vs flat-rate DSL; and 128 kbps vs multi-Mbps ADSL on the SAME copper pair. Good engineering ≠ market success — timing and economics matter.

## Slide 15
Decline and Legacy
Where ISDN went — and what it left behind
ISDN in Telecommunication · Dept. of ICE, DIU
1984–88
ITU-T I-series standards published (Red/Blue Books)
1990s
Peak deployment: SOHO Internet, PBX trunks, broadcast audio
2000s
ADSL & cable deliver Mbps on the same copper — ISDN data fades
2010s–now
Operators migrate PSTN/ISDN to all-IP (VoIP, SIP trunking); networks switched off across Europe
Why we still study it: ISDN gave us the DSL concept (digital signals on the local loop), Q.931 signalling that lives on in ISUP/SIP interworking and PRI trunks still used by PBXs, and the blueprint for today's integrated all-IP networks.
Notes: ISDN is legacy technology, but its DNA is everywhere: (1) DSL literally means Digital Subscriber Line — the term and 2B1Q line-coding research came from ISDN; (2) Q.931 messages map to SIP methods (SETUP↔INVITE, DISCONNECT↔BYE) — useful when students later meet VoIP; (3) E1 PRI trunks still connect many PBXs in Bangladesh today. Mention local context: BTCL's network followed the E1/European standards.

## Slide 16
Summary: Key Points to Remember
ISDN in Telecommunication · Dept. of ICE, DIU
ISDN
End-to-end digital network integrating voice + data on the existing telephone loop (ITU-T, 1984).
Channels
B = 64 kbps user traffic · D = 16/64 kbps signalling · H = high-rate bundles (384 k / 1536 k / 1920 kbps).
Access
BRI = 2B+D = 144 kbps (192 kbps line rate) · PRI = 23B+D (T1, 1.544 Mbps) or 30B+D (E1, 2.048 Mbps).
Reference model
TE2 –R– TA –S– NT2 –T– NT1 –U– Exchange; TE1 connects directly at S.
Protocols
D channel: I.430/431 → LAPD (Q.921) → Q.931 call control. B channel: layer 1 only.
Legacy
Superseded by DSL/fibre/VoIP, but its concepts (digital loop, out-of-band signalling) underpin them.
Notes: Recap slide — read each row aloud and cold-call students to expand one item each. The three numbers they must never forget: 64 kbps (the B channel / PCM voice rate), 144 kbps (BRI user rate) and 2.048 Mbps (E1 PRI).

## Slide 17
Review Questions
Define ISDN and explain the design goals that distinguish it from the analog PSTN.
Compare BRI and PRI: channel structure, bit rates and typical applications. Compute the line rate of an E1 PRI.
Draw the ISDN reference model, labelling all functional groups and reference points R, S, T and U.
Distinguish bearer, tele- and supplementary services, giving two examples of each.
Describe the D-channel protocol stack and outline the Q.931 message flow for a voice call.
“ISDN was an engineering success but a market failure.” Discuss.
Reading: Stallings, ISDN & Broadband ISDN with Frame Relay and ATM · Forouzan, Data Communications & Networking (ISDN chapter) · ITU-T I.120, I.430, Q.931
Thank you — questions?
Notes: Assign Q2 and Q3 as homework (numerical + diagram). Q6 is a good viva/discussion question. Announce next lecture topic (e.g. DSL family / SS7 signalling), which builds directly on today's concepts.